Placing 1 router behind another!

The SIMPLE method,

OK, why in the WORLD would you want to do THIS? Well actually there are a few reasons:

    - The most obvious, and the case for me; you have a 4 port router; all your ports are full.

    - Your 1st router is supplied by your ISP and you're required to use it, but your 2nd router has a better wireless range.

    - You need more ports and all you have are more routers, no switches. Easiest way to add more without spending $$$$$

The setup:

    - CURRENTLY you have a router from your ISP, it is DHCP active and everyone plugged in gets connected to the router and the internet.

    - You plug your Linksys router (these steps MAY work for other brands, but my experience is limited to Linksys.

    - UNPLUG the Linksys router from ANYTHING that it is plugged into, power, the1st router, ANYTHING, and everything.

    - Once you have had the power disconnected for enough time to have passed fir the device to reset, mine took 30 minutes), plug the power back into the Linksys router.

      - My router HAS a reset button that I tried to use several times; it just never seemed to work past the 1st time.

      - While it’s unplugged, go ahead and press and hold the reset button for 30 seconds.

    - Once all your lights have “settled down” plug in ONE pc to ONE of the Ethernet ports on the back of the router.

    - Open a browser, with pop ups allowed, and navigate to http://192.168.1.1 -this is the default ip address of the router.

    - Once you login, the userid is blank and the password is admin, you can work on the router setup steps.

    - Step 1 is to change the LAN IP address of the Linksys router from 192.168.1.1 to a FREE address in your LAN.

      - Typically you can find this by going to the configuration page of the FIRST device.

      - I always try and make it an address FAR enough in the back of the line that it’s easy to remember, and it should be open.

    - Disable the DHCP Server for the Linksys router

    - Save your changes

      - Step 8, change the routers ip address

      - Step 9 Disable the DHCP server

      - Step 10 Save your changes

    - Once you have received the message that your changes were successfully changed, you can NOW plug a TRADITIONAL Ethernet cable from ONE of the open ports on Router 1 to one of the open ports on the Linksys router.

      - Since most contemporary routers have “smart “ switches built into their temporary uplink or internet ports you will want to AVOID plugging into those and instead plug into the traditional Ethernet jack on the back.

    - After the IP addresses have had a chance to reset on your pc’s you should now have internet access, as well as share level access to all available pc’s both wired and wireless.